Board Bringup for Olimex Olinuxino Micro A-13
SOC- Allwinner A-13 (A-13 is not ARM cortex A13)

1.Download Allwinner A-13 datasheet and read sections that will help in board bringup.

2.To make the board working we need
Toolchain
Bootloader
Kernel image
OS (file system)

3.Download a pre built toolchain from linaro or mentor graphics and install it.Then export path where tool chain is present.
~$ export PATH=TOOLCHAIN/tools/bin:$PATH

Toolchain from scratch is different topic. Steps to build that is not mentioned here.

4.Download U-boot from github sunxi uboot
read /u-boot-sunxi/arch/arm/cpu/armv7/start.S
read /u-boot-sunxi/arch/arm/cpu/armv7/lowlevel_init.S

Preparing uboot(these steps depend on board type, may not be applicable to other board)
~$ chmod 777 mkconfig
~$ chmod 777 tools/script/make-asm-offset (path of this file?)
In new uboot source code this is moved to Kbuild in topmost directory.
~$ make ARCH=arm CROSS_COMPILE=arm-unknown-linux-gnueabi-
A13-OlinuXino-Micro_config
~$ make ARCH=arm CROSS_COMPILE=arm-unknown-linux-gnueabi-
A13-OLinuXino_config
-this is present in uboot top level directory file boards.cfg
-at the end to use all the tools available in the bin directory
~$ make ARCH=arm CROSS_COMPILE=arm-unknown-linux-gnueabi-

the last two steps will make uboot.lds, uboot.bin, uboot_spl.bin(first stage bootloader)
uboot_spl.bin loads uboot.bin

inside uboot /tools/mkimage export this path,this will make the kernel compressed image

5.Kernel
Download kernel zip or clone it using git
cd to kernel directory

~$make ARCH=arm CROSS_COMPILE=arm-unknown-linux-gnueabi- a13_defconfig

config files are present in linux/arch/[platform]/configs
/arch/arm/configs
sun5i_defconfig
a13_defconfig

~$make ARCH=arm CROSS_COMPILE=arm-unknown-linux-gnueabi- menuconfig
enable Device Drivers -> Network device support -> Wireless LAN-> realtek 8188E usb wifi
enable Device Drivers -> Network device support -> USB Network Adapters -> Davicom DM 9601
open .config file and change #GPIO_UGLY to GPIO_UGLY=y

disable mali driver and frame buffer if LCD is not plugged into the board.

~$make ARCH=arm CROSS_COMPILE=arm-unknown-linux-gnueabi- uImage
remember to export the mkimage path, otherwise the uImage will not be created

console output
LD arch/arm/boot/compressed/vmlinux
  OBJCOPY arch/arm/boot/zImage
  Kernel: arch/arm/boot/zImage is ready
  UIMAGE arch/arm/boot/uImage
"mkimage" command not found - U-Boot images will not be built
make[1]: *** [arch/arm/boot/uImage] Error 1
make: *** [uImage] Error 2

CALL scripts/checksyscalls.sh
  CHK include/generated/compile.h
  CHK kernel/config_data.h
  Kernel: arch/arm/boot/Image is ready
  Kernel: arch/arm/boot/zImage is ready
  UIMAGE arch/arm/boot/uImage
Image Name: Linux-3.4.103-00033-g9a1cd03-dir
Created: Wed May 6 07:44:23 2015
Image Type: ARM Linux Kernel Image (uncompressed)
Data Size: 4103392 Bytes = 4007.22 kB = 3.91 MB
Load Address: 40008000
Entry Point: 40008000

~$make ARCH=arm CROSS_COMPILE=arm-unknown-linux-gnueabi- INSTALL_MOD_PATH=out modules

we don't want the modules to be installed in standard path,so we mentioned “out”.

~$make ARCH=arm CROSS_COMPILE=arm-unknown-linux-gnueabi- INSTALL_MOD_PATH=out modules_install

6.Preparing the SD card
Insert the SD card in the system and find the device node for the SD card and all the partitions on the SD card
~$fdisk -l
if device node is mmcblk0. Create partitions in SD card
~$sudo fdisk -u=sectors /dev/mmcblk0

make 2 primary partitions 1st one starting from 2048 to 34815 and 2nd one starting from 34816

~$ dd if=spl/sunxi-spl.bin of=${card} bs=1024 seek=8
~$ dd if=u-boot.bin of=${card} bs=1024 seek=32

As an alternative, you can use the combined u-boot-sunxi-with-spl.bin:
~$ dd if=u-boot-sunxi-with-spl.bin of=${card} bs=1024 seek=8

7.File system

mele_debian_armhf_minimal.cpio.gz
~$ gunzip -dk mele_debian_armhf_minimal.cpio.gz
~$ sudo cpio -idv < /home/ankur/olimex/olimex_files/rootfs/mele_debian_armhf_minimal.cpio